## Slide 1: Directional Screens
Michal Piovarči1,2
Michael Wessely3
Michał Jagielski1
Mark Alexa4
Wojciech Matusik5
Piotr Didyk1,2
1Saarland University, MMCI
2MPI Informatik
3Inria, Université Paris-Saclay
4TU Berlin
5MIT CSAIL
Notes: Thanks for the introduction. Good morning my name is Michal and I will tell you about our directional screen project.

## Slide 2: Motivation
Notes: Cinemas strive for higher energy efficiency to reduce maintenance cost. Lately many advancements were made in more efficient projectors. Yet, the second important piece, the cinema screen remains unchanged since the introduction of silver screens.
(animation) Current silver screens are focusing the projection towards the audience.
(animation) However, due to imperfections light is still reflected towards the floor, walls, and ceiling.

## Slide 3: Motivation
Notes: On the other hand ideal cinema screen should reflect the light only towards the audience. And in fact we should not see the screen on this picture since the camera is outside the audience. In this talk, I will demonstrate our technique for designing and manufacturing such a screen. First, lets take a closer look at current screens.

## Slide 4: Matte Screens
Notes: The first cinema screen(s) were matte and reflected light everywhere uniformly.

## Slide 5: Silver Screens
Notes: Later they were replaced by todays standard silver screens that focus light towards the audience.

## Slide 6: Ideal Screens
Notes: An ideal screen should push this concept even further and reflect the light only towards the audience.

## Slide 7: Matte Screen Luminance
Screen
Luminance
Uniform screen luminance
Inefficient use of light
  Reflections outside the audience
Notes: Lets get more into details.
(animation) When the projector illuminates a matte screen it behaves like a Lambertian surface and reflects light everywhere uniformly.
(animations) This is very nice as the screen luminance is constant across the screen as well as from different positions in the audience. However, a considerable portion of the light is wasted.

## Slide 8: Silver Screen Luminance
Screen
Luminance
Focuses light towards the audience
Hot-spotting artifact
Uneven luminance across the audience
Notes: (animation) Silver screens improve light efficiency by focusing the light towards the viewers.
(animation) the disadvantage of this approach is that the luminance is not constant and has a peak when directly looking at the screen. This is the infamous hot-spotting artifact.
(animations) To make matters worse the hot-spot moves with the viewing location and viewers at the edge of the audience see a darker image than viewers in the middle.

## Slide 9: Ideal Screen Luminance
Screen
Luminance
Uniform luminance
Spatially-varying reflectance
Notes: Now lets derive how an ideal screen should behave. We want to reflect light uniformly to all viewers.
(animation) We can trace the amount of light that should be reflected to each viewer.
(animation) The key observation here is that the reflectance has to be spatially-varying to guarantee uniform luminance. So we will like to design a screen surface with spatially-varying reflectance.

## Slide 10: Cook-Torrance Model
Geometrical approach: surface composed of micromirrors
Distribution defines reflectance
Surface
Micromirrors
Notes: We use geometrical approach to this problem based on the reflectance model proposed by Cook & Torrance.
(animation) We assume that each surface is composed of tiny micromirrors and that the statistical distribution of these mirrors defines the reflectance.
(animation)

## Slide 11: Ideal Screen Luminance
Screen
Luminance
Uniform luminance
Spatially-varying reflectance
Micromirrors
Notes: Now one can design a set of mirrors to match the desired reflectance. What makes the problem interesting is that this distribution has to vary in space to achieve the spatially-varying reflectance.

## Slide 12: Ideal Screen Luminance
Screen
Luminance
Uniform luminance
Spatially-varying reflectance
Micromirrors

## Slide 13: Ideal Screen Luminance
Screen
Luminance
Uniform luminance
Spatially-varying reflectance
Micromirrors

## Slide 14: Previous Work
Reflectance Fabrication
Weyrich et. al.
Coleman et. al.
Engineered Screens
Notes: This idea was already exploited in previous work

## Slide 15: Reflectance Fabrication
Screen
Maximally-continuous and valley-minimizing height field
Hard non-convex problem: infeasible for large screens
Notes: The general idea was to generate a height-field matching the distribution. However, due to self-occlusions this is a hard, non-convex problem which is infeasible to solve for such large surface as a cinema screen.

## Slide 16: Convex Microgeometry
Arrange mirrors to create a convex polyhedra
Self-reflection can not occur
Screen
Notes: We propose to not generate an arbitrary height-field but a convex geometry. Such geometry will be free of self-shadowing and self-occlusions.

## Slide 17: Our Goal
Notes: So in short: our idea is to create a large screen surface build of tiny, convex geometries that are designed to reflect the light uniformly only towards the audience.

## Slide 18: Screen Generation Pipeline
Define
Cinema Arrangement
Generate
Screen Shape and Surface
Compute Microgeometries
Manufacture
Screen
Notes: In more detail we start by identifying the properties of each microgeometry. Then we will design an algorithm for generating microgeometries suitable for covering a cinema screen. Once we can generate a single geometry we will look how we can assemble them into a continuous surface. Finally, we will also manufacture a prototype screen.

## Slide 19: Setup Definition
Projector
  Assumed to be a point light source
Notes: As the input we have the projector which we assume to be a point light source.

## Slide 20: Setup Definition
Projector
  Assumed to be a point light source
Audience
  Specified as one or more polyhedra
Notes: Next, we have the audience that is defined by one or multiple polyhedra.

## Slide 21: Setup Definition
Projector
  Assumed to be a point light source
Audience
  Specified as one or more polyhedra
Screen
  Defined by its dimensions and microgeometry size
Notes: And finally we have the screen that is specified by its size and the size of a microgeometry

## Slide 22: Screen Generation Pipeline
Define
Cinema Arrangement
Generate
Screen Shape and Surface
Compute Microgeometries
Manufacture
Screen
Notes: Now we can take a closer look how to compute a single microgeometry.

## Slide 23: Screen Generation Pipeline
Define
Cinema Arrangement
Generate
Screen Shape and Surface
Compute Microgeometries
Manufacture
Screen

## Slide 24: Our Input
Directions towards the audience = mirror normals
Screen
Mirror normals
Notes: (animation) For each location on the screen we know the directions in which we would like to reflect the light. That is directions from the particular location to each point in the audience.
(animation) These directions define the normal of the micromirrors we would like to generate.

## Slide 25: Our Input
Directions towards the audience = mirror normals
Amount of light = mirror areas
Screen
Mirror normals + areas
?
Notes: (animation) We also know the amount of light we have to send in each direction to achieve uniform luminance. This specifies the areas of our micromirrors.
(animation) The last question is how to assemble a convex geometry from this input?

## Slide 26: Extended Gaussian Images
Screen
Input: a set normals and a set of areas
Constraint:
Mirror normals + areas
?
Notes: We will use the theory of Extended Gaussian Images. Minkowski showed that given a set of normals and corresponding areas one can uniquely construct a convex polyhedron. The only constraint is that the weighted sum of area times normal should sum up to zero.
This is good as we already have a set of normals (animation) and a set of corresponding areas (animation). (animation) However, as we can see all our normal are pointing towards the audience. Therefore, they don’t sum up to zero.

## Slide 27: Extended Gaussian Images
Screen
Input: a set normals and a set of areas
Constraint:
Efficient convex optimization [Little 1983]
Mirror normals + areas
?
✓
Notes: It turns out that this missing piece we have to add to satisfy the constraint is the base of the geometry which does not modify the reflectance as it is not facing the audience. (animation) Little found that for generating such a convex polyhedron there is a convex optimization with analytically computed gradient. Lets see how the algorithm works.

## Slide 28: Geometry Computation
Input
  Normals
Notes: As input we have a set of normals
(animation) without loss in generality we can assume that the center of the polyhedron lies in worlds origin.
(animation) then the normals define cutting planes.
(animation) and we can reconstruct a convex polyhedron by intersecting these planes
(animation) This creates a polyhedron which has desired normals. But we still need to incorporate the areas

## Slide 29: Geometry Computation
Input
  Normals + areas
Notes: (animation) it turns out that the areas of each facet depend on the distance from the origin.
(animation) so by manipulating these distances we can optimize our geometry to achieve the desired facet areas.

## Slide 30: Geometry Computation
Input
  Normals + areas
Optimize
  Distances from the origin

## Slide 31: Geometry Computation
Input
  Normals + areas
Optimize
  Distances from the origin
Minimize
  Facet area difference
Notes: We can compute the change in length analytically and since this is a convex optimization it runs very fast.

## Slide 32: Generated Microgeometry
Notes: This is how the optimization looks in action. Now we have a convex geometry so lets assemble our screen.

## Slide 33: Tileability Problem
Shape is not tileable
  Leads to artifacts on the screen
We have to enforce tileability
Notes: And ouch.
(animation) we can see the shape does not cover the entire surface. We could do a number of things, try to pack the ellipsoids, or paint the empty portions with black. But we opted for a more elegant solution and that is to generate microgeometries than can be tiled.

## Slide 34: Enforcing Tileability
Tileable square shapes
Adding side-faces
What to do with areas?
Notes: And in particular we decided that they will be squares.
(animation) We achieve this by adding side-faces to our geometry. But remember we always need a normal and an area. (animation) Normals are easy, (animation) but what to do with the areas?

## Slide 35: Tileable Optimization
Constraint: distances between opposite side facets are equal
Parameters: side face areas need to be sufficiently large
Original
Added Side Faces
Sufficient Area
Constraint
Square Bounding Box
Constraint
Notes: (animation) The first options is to let them be arbitrary. The added sides slightly modify the shape but as we can see the geometry is not tileable and what’s worse it’s not even a square.
(animation) First, we add a new constraint that the distances between opposite faces have to be the same. This will force the bounding box to be a square.
(animation) Next, we also add the areas of the side-faces into our optimization. This will ensure they are sufficiently large to lift the geometry from the surface.

## Slide 36: Our Microgeometry Optimization
Input:
  Normals + areas
Constraints:
Minimize:
  Area difference
Manipulate:
  Distances from origin
+
+ square bounding box
+ side areas
Notes: Now lets recapitulate our microgeometry optimization.
(animation) Originally, the input was a set of normals and corresponding areas (animation) that satisfied the constraint that they sum up to zero. (animation) We minimized the difference of desired and current facet area (animation) by manipulating the distances of each facet from worlds origin.
(animation) Now to create a tileable geometry we add a side faces as additional input. (animation) To guarantee a square bounding box we included an additional constraint. (animation) and finally, to generate a tileable geometry we included the areas of the side faces into the optimization.

## Slide 37: Screen Generation Pipeline
Define
Cinema Arrangement
Generate
Screen Shape and Surface
Compute Microgeometries
Manufacture
Screen
Notes: Now that we know how to generate a microgeometry for a any screen location we can see how to assemble them to form a screen.

## Slide 38: Screen Generation Pipeline
Define
Cinema Arrangement
Generate
Screen Shape and Surface
Compute Microgeometries
Manufacture
Screen

## Slide 39: Screen Discretization
Notes: (animation) Our strategy is to discretize the screen into individual pixels and for each pixel generate a microgeometry.
(animation) However, on this picture we can see an additional problem we have to deal with and that is alignment of the microgeometries.

## Slide 40: Surface Alignment
Geometries follow audience
Screen
Notes: So let us use an extreme case as an example. When we have a screen it should reflect the light from each point towards the audience.

## Slide 41: Surface Alignment
Geometries follow audience
Height adjustment required
Screen
Notes: This will force the geometries to rotate towards the viewers. This rotation affects the reflections as self-shadowing and cross reflections can occur.

## Slide 42: Surface Alignment
Geometries follow audience
Height adjustment required
Poisson equation
Screen
Notes: To fix this we adjust the height of each geometry. This requires solving a standard Poisson's equation, which guarantees a smooth transition between neighbouring geometries.

## Slide 43: Surface Alignment
Geometries follow audience
Height adjustment required
Poisson equation
  Gradient field from normals
Screen
Notes: After the height adjustment our geometries move and need to be recalculated. However, it turns out the height adjustment can be computed from the normal information. So for each iteration only normal sampling is necessary. And, therefore, the screen itself is computed only once.

## Slide 44: Content Preparation
Large reflection angle = smaller perceived luminance
Directional Screen
Notes: The last bit is content preparation. Our screens reflect light uniformly towards the entire audience. We can see the size of the audience depends on the location on the screen. For example top row illuminates larger area than bottom. Since both receive the same amount of light from the projector, top will appear dimmer. This is very different from standard hot-spotting as this effect only depends on the projector, audience setup. Therefore, it is constant across the view and audience

## Slide 45: Calibration Masks
Constant across view and audience
  Correction with a transparent film / digital filter
  Modern projectors can redirect the light [Damberg 2016]
Calibration Mask
Notes: We can simply remove it by a calibration mask in front of the projector. Such naïve approach does not lead to ideal light use but we show it still outperforms current silver screens. One can also use modern projectors to retarget the light from brighter to dimmer areas and achieve even better results.

## Slide 46: Screen Generation Pipeline
Define
Cinema Arrangement
Generate
Screen Shape and Surface
Compute Microgeometries
Manufacture
Screen
Notes: Now we have come to the point where we have a whole screen assembled. Before manufacturing the screen we will validate it in simulations.

## Slide 47: Considered Designs
Theater
Conference Room
Home Theater
Notes: For our validation we considered three designs. A vanilla case theater, conference room which has larger audience than the screen and a split view home projection setup with two disjoint viewing volumes.

## Slide 48: Theater Screen
Notes: We can see that our display achieves significantly brighter peak luminance and more uniform reflection than the current standard silver screen.

## Slide 49: Conference Room Screen
Notes: In the conference room setup the peak luminance is lower. This is because we reflect the same amount of light towards a larger audience. Yet the profile is very flat.

## Slide 50: Home Theater Screen
Notes: Finally, for the split view achieves the highest peak luminance since we concentrate all the light towards two small viewing volumes.

## Slide 51: Screen Generation Pipeline
Define
Cinema Arrangement
Generate
Screen Shape and Surface
Compute Microgeometries
Manufacture
Screen
Notes: Now we can go to fabrication.

## Slide 52: Fabrication Method
Notes: We used a 3-axis CNC milling machine to mill our screens from aluminum. The aluminum was then hand polished to achieve mirror-like finish.

## Slide 53: Fabricated Prototypes - Theater
Close up
Theater Screen
20 cm
20 cm
Notes: We manufactured two prototype screens. A 20 by 20 cm patch from a cinema screen.

## Slide 54: Fabricated Prototypes – Home Theater
Close up
Home Theater Screen
7 cm
11.5 cm
Notes: And a 7 by 11.5 cm split screen.

## Slide 55: Audience Coverage - Setup
Screen
Directional Screen
Notes: For the validation we first validate the audience coverage. When a directional screen is illuminated it should reflect light towards the audience. (animation) So if we place another screen in front of the audience (animation) we will see its projection that we can capture with a camera. (animation) (the reflection of the reflection that creates the projection of the audience) :-D

## Slide 56: Theater Screen Coverage
Simulation
Prototype
Notes: Here is a comparison of simulated and manufactured theater screen reflections, compared to ideal reflection marked by green square.

## Slide 57: Home Theater Screen Coverage
Simulation
Prototype
Notes: And the same for home-theater screen were we can see the split audience

## Slide 58: Patch Reflection - Setup
Notes: Not only the entire screen should illuminate the audience uniformly but also individual geometries. To validate this claim we moved a small patch on the screen and captured the corresponding reflection.

## Slide 59: Patch Reflection - Results
Notes: We can see that the reflection behaves nicely as we move the patch around

## Slide 60: Prototype Results
Notes: Finally, we of course project an image on the screen. We projected a static image and moved with the camera through the audience. We can see that the reflection is brightest inside the audience and quickly dims when going outside.

## Slide 61: Conclusions
Generating of tillable convex microgeometries with defined reflectance
Constructing large surfaces with spatially-varying reflectance properties
Application to screen design
The technique can be seen as more general appearance fabrication technique
Notes: In conclusion I hope you learned today something about computing tillable convex geometries with prescribed reflectance. And how to assemble such geometries to create a continuous surface. We showed an application for screen design but the same technique can be applied more generally to produce a surface with desired reflectance.

## Slide 62: Limitations
Fabrication
  Aluminum is not a mirror
  Polishing
  Accuracy of geometry
Notes: Our technique has some limitations. Mainly our proof of concept fabrication technique. This did not produce ideal results since aluminum violates our ideal mirror assumption. Also manual polishing rounded of fine edges and lowered the accuracy of our geometries. This is mostly visible in the split audience where a perfect edge is required.

## Slide 63: Thanks for Your Attention!
W. Matusik
P. Didyk
M. Piovarči
M. Alexa
M. Wessely
M. Jagielski